## Slide 1: Electric Water Heater System

## Slide 2: Team members
ZYAD WALED ELBRDAN

## Slide 3: agenda
Introduction
Features and Specifications
System Design
Flowchart
Workflow

## Slide 4: Introduction
Objective: Design and implement an electric water heater with the following functionalities:
Temperature setting and control.
ON/OFF behavior management.
Accurate temperature sensing.
Automated heating and cooling element control.
User-friendly display using seven-segment indicators.
Indicator LED for heating status.

## Slide 5: Features and Specifications
1. Temperature Setting
"Up" and "Down" buttons adjust the required water temperature.
First button press activates temperature setting mode.
Temperature adjustments:
"Up" increases by 5°C (max: 75°C).
"Down" decreases by 5°C (min: 35°C).
Temperature is saved to external EEPROM.
Automatically exits setting mode after 5 seconds of inactivity.
Default temperature: 60°C.

## Slide 6: Features and Specifications
2. ON/OFF Behavior
"Initial state: OFF when power is connected.
Toggle ON/OFF using the "ON/OFF" button.
In OFF state:
Heater components and displays are disabled.

## Slide 7: Features and Specifications
3. Temperature Sensing
Measures water temperature every 100ms.
Maintains average of the last 10 readings.
Accurate sensing for decision-making.

## Slide 8: Features and Specifications
4. Heating and Cooling Element Control
Heating Element:
ON: Current temperature < Set temperature - 5°C.
OFF: Current temperature > Set temperature + 5°C.
Cooling Element:
OFF: Current temperature < Set temperature - 5°C.
ON: Current temperature > Set temperature + 5°C.

## Slide 9: Features and Specifications
5. Seven-Segment Display
Default: Displays current water temperature.
Temperature setting mode:
Displays set temperature.
Blinks every 1 second.
Exits mode if no buttons are pressed for 5 seconds.

## Slide 10: Features and Specifications
6. Heating Element LEDs
Heating led Blinks every 1 second when heating element is ON.
Cooling led Remains ON if cooling element is active.
Booth leds OFF if the temperature is prefect or the system is off

## Slide 11: System Design

## Slide 12: Hardware Components
Microcontroller: ATMEGA32.
Temperature Sensor: Measures water temperature.
EEPROM: for storing set temperature.
Seven-Segment Display: Shows current/set temperature.
Heating and Cooling Elements: Regulate water temperature.
LED Indicator: Displays heating status.

## Slide 13: Software Modules
HAL (Hardware Abstraction Layer):
The HAL provides an interface for hardware components. It abstracts the hardware specifics, making the system more modular and scalable.
Key modules in the HAL include:
Buttons: Handles button press detection and debouncing.
EEPROM: Interfaces with the 24C16B for reading and writing set temperature data.
Seven-Segment Display: Manages the display of temperature values, including blinking behavior.
LEDs: Controls the status indication of heating and cooling operations.
LM35: Temperature sensor used to get the water temperature .
MCAL (Microcontroller Abstraction Layer):
The MCAL provides low-level drivers for the ATMEGA32 microcontroller. It ensures efficient and reliable hardware operation.
Key drivers in the MCAL include:
GPIO (General Purpose Input/Output): Configures and controls digital I/O pins.
Timers: Used for periodic tasks such as temperature sensing and LED blinking.
ADC (Analog-to-Digital Converter): Reads analog data from the temperature sensor and converts it to a digital format.
I2C Protocol: Implements communication protocols for interfacing with the external EEPROM.

## Slide 14: Flowchart

## Slide 15: Flowchart

## Slide 16: IO List

## Slide 17: IO List

## Slide 18: Workflow
Power ON: System initializes in OFF state.
User toggles ON state:
Current water temperature displayed.
Heating or cooling elements activated based on temperature.
User adjusts temperature:
"Up" and "Down" buttons change settings.
EEPROM saves new set temperature.
Real-time temperature sensing:
Ensures water remains within desired range.
Heating and cooling elements respond dynamically.
Visual feedback:
Seven-segment display for temperature.
LED indicator for heating status.

## Slide 19: Component Used
1. 24C08EEPROM.
2. Tempsensor(LM35).
3. CoolingElement.
4. HeatingElement.
5. 7-segments.
6. LEDs.
7. PushButtons.
8. SolidState Relays

## Slide 20: Thank you
Zyad Waled